## Slide 1: Image processing
معالجه صور

## Slide 2: Introduction image processing

## Slide 3
“One picture is worth more than ten thousand words”
Anonymous

## Slide 4
Image Processing
image in →image out
Image Analysis
image in →measurements out
Image Understanding
image in →high-level description out
Image Processing , Image Analysis , Image Understanding

## Slide 5
Environment
Acquisition
Filter
Segmentation
Enhancement
Report

## Slide 6: Environment
Filed
Electronic spectrum
sound
Media
Indoor
Outdoor
Under water
Coordinate
الاسقاط(ثنائي ,ثلاثي)

## Slide 7: What Is An image ?
An image is a two-dimensional function, f(x,y), where x and y are spatial (plane) coordinates, and the amplitude of f(x,y) at any pair of coordinates (x, y) is called the intensity or gray level of the image at the point (x,y).
Note: When x, y, and the amplitude values of f are all finite, discrete quantities, we call the image a digital image.

## Slide 8: What Is A digital Image ?
A digital image is a two-dimensional matrix, f(M,N), where the value at the location (x,y) is called the intensity or gray level of the image at the point (x,y).
So, the digital image is composed of a finite number of elements, each of which has a particular location and value.
The digital image elements are referred to pels, and pixel

## Slide 9: What Is A digital Image ?
الصورة الرقمية عبارة عن مصفوفة ثنائية الأبعاد ، f(M,N), حيث تسمى القيمة في الموقع (x,y) الكثافة أو المستوى الرمادي للصورة عند النقطة (x,y).
لذلك ، تتكون الصورة الرقمية من عدد محدود من العناصر ، لكل منها موقع وقيمة معينة.

## Slide 10: What Is A digital Image ?

## Slide 11: Image Sampling and Quantization
An image may be continuous with respect to the x- and y-coordinates, and also in amplitude. To convert it to digital form, we have to sample the function in both coordinates and in amplitude.
Digitizing the coordinate values is called sampling.
Digitizing the amplitude values is called quantization.
How do we get a clearer picture?

## Slide 12: Sampling , quantization

## Slide 13: What Is A digital Image ?

## Slide 14: What Is A digital Image ?

## Slide 15: What Is Digital Image Processing?
Digital image processing field, is a preprocessing step for other computerized processing fields such as computer vision and pattern recognition.
In computer vision, the goal is to use computers to emulate human vision, including learning (understanding) and being able to make inferences and take actions based on visual inputs.
مجال معالجة الصور الرقمية ، هو خطوة معالجة مسبقة لمجالات المعالجة المحوسبة الأخرى مثل رؤية الكمبيوتر والتعرف على الأنماط.
في رؤية الكمبيوتر ، الهدف هو استخدام أجهزة الكمبيوتر لمحاكاة الرؤية البشرية ، بما في ذلك التعلم (الفهم) والقدرة على عمل الاستنتاجات واتخاذ الإجراءات بناءً على المدخلات المرئية.

## Slide 16: Applications of Digital Image Processing
Image sharpening and restoration
It refers to the process in which we can modify the look and feel of an image. It basically manipulates the images and achieves the desired output. It includes conversion, sharpening, blurring, detecting edges, retrieval, and recognition of images.
2) Medical field
There are several applications under medical field which depends on the functioning of digital image processing .Gamma-ray imaging,X-Ray Imaging,Medical CT scan ,UV imaging
3) Robot vision
There are several robotic machines which work on the digital image processing. Through image processing technique robot finds their ways, for example, hurdle detection root and line follower robot.

## Slide 19: Applications of Digital Image Processing
4) Pattern recognition
It involves the study of image processing, it is also combined with artificial intelligence such that computer-aided diagnosis, handwriting recognition and image recognition can be easily implemented. Now a days, image processing is used for pattern recognition.
5)Video processing
It is also one of the applications of digital image processing. A collection of frames or pictures are arranged in such a way that it makes the fast movement of pictures. It involves frame rate conversion, motion detection, noise reduction and color space conversion etc.

## Slide 20: Cont.,
There are no clear-cut boundaries in the continuum from image processing at one end to computer vision at the other.
So, we can consider three types of computerized processes in this continuum: low-, mid-, and high-level processes.
Low-Level
Mid-Level
High-Level

## Slide 21: Cont.,
Low-level processes involve primitive operations such as noise reducing, contrast enhancement, and image sharpening.
Mid-level processing on images involves tasks such as segmentation, description of those objects to reduce them to a form suitable for computer processing.
Higher-level processing involves “making sense” of an ensemble of recognized objects, as in image analysis, and, at the far end of the continuum, performing the cognitive functions.
Thus, digital image processing encompasses processes whose inputs and outputs are images and, in addition, encompasses processes that extract attributes from images, up to and including the recognition of individual objects.

## Slide 22: The Origins of Digital Image Processing
One of the first applications of digital images was in the newspaper industry, when pictures were first sent by submarine cable between London and New York (Bartlane cable).
- produced in 1921 (telegraph)
- five distinct levels of gray
- produced in 1922 (telegraph)
- after the signals had crossed the Atlantic twice
- produced in 1929 (telegraph)
- 15 distinct levels of gray

## Slide 23: The Origins of Digital Image Processing
The history of digital image processing is intimately tied to the development of the digital computer

## Slide 24: Cont.,
The first computers powerful enough to carry out meaningful image processing tasks appeared in the early 1960s.
- In 1964 when pictures of the moon transmitted by Ranger 7.
- processed by a computer to correct various types of image distortion inherent in the on-board television camera.
ي عام 1964، قامت مركبة رينجر 7 بالتقاط ونقل صور للقمر. تم التقاط هذه الصور باستخدام كاميرا تلفزيونية موجودة على متن المركبة. ومع ذلك، كانت الصور التي تم استلامها من رينجر 7 تعاني من أنواع مختلفة من التشوهات في الصورة ناتجة عن عيوب الكاميرا وأخطاء النقل.
لتصحيح هذه التشوهات وتحسين جودة الصور، تم استخدام تقنيات معالجة الصور عن طريق الحاسوب. تم تحويل الصور إلى تنسيق رقمي وإدخالها إلى نظام حاسوبي، حيث تم استخدام خوارزميات وبرامج لأداء تصحيح وتحسين الصور.

## Slide 26: Image Types
Image types according to color :
1-color RGB
2-Binary
3-gray

## Slide 27: Binary image

## Slide 28: gray image

## Slide 29: RGB Image

## Slide 30: Image Types
Image types according to energy source:
1- Electromagnetic energy spectrum images(لصور الخاصة بطيف الطاقة الكهرومغناطيسية هي صور تلتقط مجموعة متنوعة من الموجات أو الترددات ضمن طيف الطاقة الكهرومغناطيسية. يشمل طيف الطاقة الكهرومغناطيسية مجموعة واسعة من الطاقة، بدءًا من الموجات الراديوية ذات التردد المنخفض إلى الأشعة الغاما ذات الطاقة العالية. )
2- Acoustic & ultrasonic images( الصور الطبية التي تتم إنشاؤها باستخدام الموجات فوق الصوتية. تستخدم هذه التقنية الموجات فوق الصوتية لإنشاء صور داخلية للأنسجة والأعضاء في الجسم.)
3- Electronic images(لصور الإلكترونية هي صور تم إنشاؤها أو تخزينها بواسطة أجهزة إلكترونية وتكنولوجيا الحوسبة. )
4- Computer modeling images (الرسام )

## Slide 31: Electromagnetic spectrum (EM)
Electromagnetic waves are sinusoidal waves of varying wavelengths, or are a stream of massless particles, each traveling in a wavelike pattern and moving at the speed of light.
Each massless particle contains a certain amount (or bundle) of energy (photon)

## Slide 32: Electromagnetic spectrum (EM)

## Slide 33: light
Light is a form of electromagnetic radiation that is visible to the human eye and can travel through both vacuum and material mediums. It is part of the electromagnetic spectrum, which includes various types of radiation such as infrared, ultraviolet, X-rays, and gamma rays
0.43 micron (violet) to about 0.79 micron (red).
violet, blue, green, yellow, orange, and red

## Slide 34: Fundamental steps in digital image processing.

## Slide 35: Fundamental steps in digital image processing.

## Slide 36: Fundamental steps in digital image processing.

## Slide 37: Fundamental steps in digital image processing.

## Slide 38: Fundamental steps in digital image processing.

## Slide 39: Fundamental steps in digital image processing.

## Slide 40: Fundamental steps in digital image processing.

## Slide 41: Fundamental steps in digital image processing.

## Slide 42: Elements of Visual Perception 1.Structure of the Human Eye
E
Retina:(2 receptors)
- Cones (6 – 7 million) بكسل الجوال
- Rods (75 to 150 million)
*photopic or bright-light vision
scotopic or dim-light vision
Notes: شبكية العين تتكون من مستقبلين هما :
- المخاريط
(6 – 7 million)
* رؤية ضوئية أو ضوء ساطع.
- عصي
(75 to 150 million)
* رؤية ظلامية أو رؤية ضوء خافت.

## Slide 43: Image Formation in the Eye

## Slide 44: What determines image quality?
(Achromatic or monochromatic) and chromatic light.
Three basic quantities are used to describe the quality of a chromatic light source: radiance; luminance; and brightness.
Radiance
is the total amount of energy that flows from the light source, and it is usually measured in watts.
Luminance,
measured in lumens (lm), gives a measure of the amount of energy an observer perceives from a light source.
Brightness
Brightness is a subjective perception of light intensity by the human visual system. It is the attribute of visual perception that determines the subjective impression of how intense a light source or a surface appears. Brightness can be influenced by various factors, including the luminance of the light source or surface, the surrounding environment, and individual differences in visual perception. Brightness is often described using qualitative terms such as "bright," "dim," or "dull.«في الحاسوب ناخذ تدرج اللون لكل نقطه

## Slide 45: Some well known optical illusions بعض الخداع البصري المعروف

## Slide 46: Some well known optical illusions simultaneous contrast

## Slide 47: Next
Image Sensing and Acquisition استشعار الصورة والحصول عليها

## Slide 48
Pinhole projection

## Slide 50
Notes: ايش اسم النقطه
ما السبب

## Slide 54: Image Sensing and Acquisition
Image Sensing and Acquisition There are 3 principal sensor arrangements (produce an electrical output proportional to light intensity). (i)Single imaging Sensor (ii)Line sensor (iii)Array sensor

## Slide 55: Image Sensing and Acquisition

## Slide 56: Image Sensing and Acquisition
1.Image Acquisition Using a Single Sensor.
2.Image Acquisition Using Sensor Strips 3. Image Acquisition Using Sensor Arrays

## Slide 57: 1.Image Acquisition Using a Single Sensor
In order to generate a 2-D image using a single sensor, there have to be relative displacements in both the x- and y-directions between the sensor and the area to be imaged. An arrangement used in high precision scanning, where a film negative is mounted onto a drum whose mechanical rotation provides displacement in one dimension. The single sensor is mounted on a lead screw that provides motion in the perpendicular direction. Since mechanical motion can be controlled with high precision, this method is an inexpensive (but slow) way to obtain high-resolution
images.

## Slide 58: 1.Image Acquisition Using a Single Sensor
من أجل إنشاء صورة ثنائية الأبعاد باستخدام مستشعر واحد، يجب أن تكون هناك إزاحات نسبية في كلا الاتجاهين x وy بين المستشعر والمنطقة المراد تصويرها. وهو ترتيب يستخدم في المسح الضوئي عالي الدقة، حيث يكون الفيلم سلبيًا يتم تركيبه على أسطوانة يوفر دورانها الميكانيكي إزاحة في بُعد واحد. يتم تثبيت المستشعر الفردي على برغي رئيسي يوفر الحركة في الاتجاه العمودي. وبما أنه يمكن التحكم في الحركة الميكانيكية بدقة عالية، فإن هذه الطريقة تعتبر طريقة غير مكلفة (ولكنها بطيئة) للحصول على دقة عالية
الصور.

## Slide 59: 2.Image Acquisition Using Sensor Strips
عملية الحصول على الصور باستخدام شرائح الاستشعار تشير إلى عملية التقاط الصور باستخدام مجموعة خطية من أجهزة الاستشعار المرتبة في شريط أو خط واحد. يتم استخدام هذا النهج بشكل شائع في أنظمة التصوير المختلفة، بما في ذلك الماسحات الضوئية المسطحة وتطبيقات التصوير الجوي والتصوير الطبي والصناعي.
في حالة الماسحات الضوئية المسطحة، يتم استخدام شريط استشعار واحد لمسح الوثيقة أو الصورة. يتكون الشريط الاستشعار من مجموعة خطية من أجهزة الاستشعار الحساسة للضوء. يتم وضع الوثيقة أو الصورة على سطح الماسح الضوئي، ويتحرك الشريط الاستشعار عبر الوثيقة، مع التقاط الصورة سطراً بسطر.
وفي حالة التطبيقات الجوية، يتم استخدام أشرطة استشعار خطية للاستجابة لمختلف نطاقات الطيف الكهرومغناطيسي، وتركيبها عمودياً على اتجاه الطيران الثابت للحصول على صورة للمنطقة الجغرافية المستهدفة. تعطي شريط الاستشعار سطرًا واحدًا من الصورة في كل مرة، وتكتمل البُعدين الآخرين للصورة ثنائية الأبعاد بحركة الشريط.

## Slide 60: Image Acquisition Using Sensor Arrays
تم العثور على هذا النوع من الترتيب في الكاميرات الرقمية. المستشعر النموذجي لهذه الكاميرات هو مصفوفة CCD، والتي يمكن تصنيعها بنطاق واسع من خصائص الاستشعار ويمكن تعبئتها في مصفوفات متينة مكونة من 4000 * 4000 عنصر أو أكثر. تُستخدم مستشعرات CCD على نطاق واسع في الكاميرات الرقمية وأدوات استشعار الضوء الأخرى. تتناسب استجابة كل مستشعر مع تكامل الطاقة الضوئية المسقطة على سطح المستشعر، وهي خاصية تستخدم في التطبيقات الفلكية وغيرها من التطبيقات التي تتطلب صورًا منخفضة الضوضاء.

## Slide 61: A Simple Image Formation Model
An image is a two-dimensional function of the form f(x, y). f(x, y) must be nonzero and finite
0 < f(x,y) < infinit
f(x, y) may be characterized by two components: (1) the amount of source illumination incident on the scene being viewed, and (2) the amount of illumination reflected by the objects in the scene. Appropriately, these are called the illumination and reflectance.
f(x, y)=i(x, y)r(x, y)

## Slide 62: A Simple Image Formation Model
0 < i(x,y) < infinite
0 < r(x,y) < 1
gray level (l) : f(x0,y0)=l
Lmin <l< Lmax
Lmin=imin*rmin
Lmax=imax*rmax
Gray scale : [Lmin,Lmax] and shifted to [0,L-1]

## Slide 63: Image Sampling and Quantization

## Slide 64: Image Sampling and Quantization

## Slide 65: Image Sampling and Quantization

## Slide 66: An image f(x, y) is sampled so that the resulting digital image has M rows and N columns. The values of the coordinates (x, y) now become discrete quantities. Thus, the values of the coordinates at the origin are (x, y)=(0, 0). The next coordinate values along the first row of the image are represented as (x, y)=(0, 1)
Representing Digital Images

## Slide 67: This digitization process requires decisions about values for M, N, and for the number, L, of discrete gray levels allowed for each pixel (M ,N and L are positive integers). Due to processing, storage, and sampling hardware considerations, the number of gray levels typically is an integer power of 2: L = 2k The Gray levels is in the interval [0,L-1]. Dynamic range of an image : the range of values spanned by the gray scale. (high dynamic range)
Representing Digital Images

## Slide 68: The number, b, of bits required to store an image is : b = M x N x K When M=N : b = N2 K We have 4-bits, 8-bits , …, images.
Representing Digital Images

## Slide 69
Representing Digital Images

## Slide 70: Spatial and Gray-Level Resolution
Sampling is the principal factor determining the spatial resolution of an image.
Spatial resolution is the smallest discernible detail in an image.
Or, it is simply the smallest number of discernible line pairs per unit distance; for example, 100 line pairs per millimeter.
Gray-level resolution refers to the smallest discernible change in gray level.
أصغر تغيير يمكن تمييزه في مستوى الرمادي.

## Slide 71: Spatial and Gray-Level Resolution

## Slide 72
Zooming and Shrinking Images

## Slide 73: Zooming and Shrinking Images
Zooming requires two steps: the creation of new pixel locations, and the assignment of gray levels to those new locations.
Simple method is Pixel replication. It is used when we want to increase the size of an image an integer number of times (Exp 2,3,..).
Pixel interpolation such as nearest neighbor interpolation. It is used when we want to increase the size of an image real number of times (Exp 1.3,2.3,..).
bilinear interpolation is another kind of Pixel interpolation and the best.

## Slide 74: Some Relationships Between Pixels
Neighbors of a Pixel :
(4-neighbors) of a pixel p at coordinates (x, y) have coordinates : (x+1, y), (x-1, y), (x, y+1), (x, y-1).
(4-diagonal neighbors) : have coordinates
(x+1, y+1), (x+1, y-1), (x-1, y+1), (x-1, y-1)
4-diagonal neighbors together with the 4-neighbors, are called the 8-neighbors of p.

## Slide 75: Some Relationships Between Pixels
Neighboring Connectivity:
two pixels are connected if they are neighbors and if their gray levels satisfy a specified criterion of similarity.تفي بمعيار محدد
Adjacency: let V a sub set of [0,L-1]

## Slide 76: Some Relationships Between Pixels
Adjacency:
Path : A (digital) path (or curve) from pixel p with coordinates (x, y) to pixel q with coordinates (s, t) is a sequence of distinct pixels with coordinates:
(x0 , y0), (x1 , y1), … , (xn , yn)
According to one of the adjacency types.

## Slide 77: Some Relationships Between Pixels
Connectivity in a region :
Let S represent a subset of pixels in an image. Two pixels p and q are said to be connected in S if there exists a path between them consisting entirely of pixels.
Connected Set:
For any pixel p in S, the set of pixels that are connected to it in S is called a connected component. If it only has one connected component, then set S is called a connected set

## Slide 78: Some Relationships Between Pixels
Region:
Let R be a subset of pixels in an image. We call R a region of the image if R is a connected set.
Boundary (also called border or contour):
A boundary of a region R is the set of pixels in the region that have one or more neighbors that are not in R.
Edge: is not closed path.

## Slide 79: Distance Measures

## Slide 80: Image Operations on a Pixel Basis
Division, addition, subtraction, …
arithmetic and logic operations are similarly defined between corresponding pixels in the images involved.

## Slide 81: Image Operations on a Pixel Basis

## Slide 82: Image Operations on a Pixel Basis

## Slide 83: Image Operations on a Pixel Basis
Four arithmetic operation are denoted as:

Images in arithmetic operations must be of the same size.

## Slide 84: Logical operations

## Slide 85: Averaging noisy images for noise reduction

## Slide 86: Averaging noisy images for noise reduction

## Slide 87: Note:
In arthmetic operations such as difference between two 8-bit images can range from a min. Of -255 and a max. Of 255 ,and the values of sum two images can range from 0 to 510.
So we need to set all negative values to 0 and set to 255 all values exceed this limit.

## Slide 88: Spatial operations
Spatial operations are performed directly on the pixels of a given image.
Point : the output value at a specific coordinate is dependent only on the input value at that same coordinate.
Local : the output value at a specific coordinate is dependent on the input values in the neighborhood of that same coordinate
Global : the output value at a specific coordinate is dependent on all the values in the input image

## Slide 89: Spatial operations

## Slide 90
Image Enhancement

## Slide 91: Image Enhancementin the Spatial Domain
The term spatial domain refers to the aggregate of pixels composing an image.
Spatial domain methods are procedures that operate directly on these pixels. denoted by
where f(x, y) is the input image, g(x, y) is the processed image, and T is an operator on f, defined over some neighborhood of (x, y).

## Slide 92: Some Basic Gray Level Transformations
Image Negatives : The negative of an image with gray levels in the range [0,L-1]is obtained by: s = L – r - 1

## Slide 93: Some Basic Gray Level Transformations
Log Transformations : maps a narrow range of low gray-level values in the input image into a wider range of output levels.
s = c log (1 + r)

## Slide 94
Image Enhancement